## Slide 1
Ben Collins
Queen’s University Belfast | School of Biological Sciences
BIO8206 – Introduction to Biological Mass Spectrometry
Fundamentals
Data Analysis Workshop
Notes: **********************************************************
******************** PRESS RECORD *********************
**********************************************************

## Slide 2: Experimental workflow for today’s data
Protein
extraction
Protein
digestion
Proteins
Peptides
Peptide
separation
time
organic
solvent, %
ESI
Ionization
HPLC
Mass
spectrometry
mass spectrometer
MS1 – mass (m/z) of peptides
MS2 – mass (m/z) of fragments
Isolation +
fragmentation
Q1 filter
TOF analyzer
Collision
cell
HeLa cells
Notes: This is a very generalized workflow that is applied by groups working on proteomics using mass spectrometers
Broadly represents the most common method

## Slide 3: 2 topics for workshop – also related to assignment!
Calculating mass from m/z
  We measure m/z but we want to know mass!
  Review charge states and isotope distributions
Interpreting fragmentation (or MS2) spectra
  Using peptide as example – but generalizable to other analytes
  Manual annotation of amino acid sequence of peptide from MS2 spectrum

## Slide 4: Recap on isotopic distributions and charge stages
2 separate issues to review:
  Elemental isotopic abundances and MS
  Using isotope distributions to determine charge state
In nature for given elements we find different isotopic abundances of various elements because or different numbers of neutrons
  We are primarily concerned with carbon
  98.9 % of the carbon in nature is 12C (6 protons + 6 neutrons in nucleus)
  1.1 % is 13C (6 protons + 7 neutrons in nucleus)
  1 part per trillion is 14C (6 protons + 8 neutrons in nucleus)
    Unstable with half life of 5,730 years  radio carbon dating
Some elemental isotope abundances

## Slide 5: Isotope Distributions
C1
C10
C50
C93
C185
C280
~18 aa
(based on average
nb of C per amino acid=5.3)
~35 aa
~52 aa
Mw of carbon is 12 Daltons
Question:
What is the natural abundance of the carbon 13 isotope?
Answer: ~1.1 %
10 x 12C
9 x 12C
1 x 13C
8 x 12C
2 x 13C

## Slide 6: Do we actually measure mass? No, mass to charge ratio
MH+
M2H++
M3H+++
m/z
counts
MH+
501.008
251.008
167.67
M2H++
M3H+++
neutral mass
mass/charge
500
500
500
501.008
251.008
167.674
mass (inc. protons)
501.008
502.016
503.024
m/z
counts
To calculate the neutral mass from the measured m/z we need to know the charge state
We use the existence of the isotopic distribution as a trick to figure out the charge state!
501
502
503
m/z
counts
251
252
253
m/z
counts
167
168
169
~1 m/z
~0.5 m/z
~0.33 m/z
MH+
M2H++
M3H+++

## Slide 7: So, if we want to calculate neutral mass from m/z… Worked example:
m/z
counts
m/z
counts
686.26
686.59
686.92
687.26
Determine charge state
spacing between istopalogues = ~0.33
=> charge state = 1 / ~0.33 = 3+
Calculate mass (with protons)
Monoisotopic mass x charge state
686.26 x 3 = 2,058.78
Calculate neutral mass
Subtract mass of protons
2,058.78 – (3 x 1.008) = 2,055.756 Da
Note: assume positive mode electrospray so we expect ionizing protons

## Slide 8: 2 topics for workshop – also related to assignment!
Calculating mass from m/z
  We measure m/z but we want to know mass!
  Review charge states and isotope distribubtions
Interpreting fragmentation (or MS2) spectra
  Using peptide as example – but generalizable to other analytes
  Manual annotation of amino acid sequence of peptide from MS2 spectrum

## Slide 9: Fragmenting a Peptide
A-P-N-D-F-N-L-K
(MH+ 919)
B-ions Y-ions
72.0 A P-N-D-F-N-L-K 847.4
169.1 A-P N-D-F-N-L-K 750.4
283.1 A-P-N D-F-N-L-K 636.3
398.2 A-P-N-D F-N-L-K 521.3
545.2 A-P-N-D-F N-L-K 374.2
659.3 A-P-N-D-F-N L-K 260.2
772.4 A-P-N-D-F-N-L K 147.1
b-ions = SAA + H+
y-ions = SAA + H2O + H+
monoisotopic masses

## Slide 10: Sequence & MS2 Spectrum – b and y ions
A
P
N
D
F
N
L
K
A
P
N
D
F
N
L
K
A-P-N-D-F-N-L-K
(MH+ 919)

## Slide 11: Amino Acid Masses

## Slide 12
Procedure
Convert the precursor m/z to single charged (e.g. M2H++  MH+)
  (If everything is singly charged it makes the math easier….)
2. Locate the peak with the biggest m/z value (i.e right most peak) and subtract that value from the precursor m/z
3. Check this value against the amino acid table (monoisotopic)
  if match then this should be one of the terminal AA residues (go to step 4)
  If no match then move onto the next biggest m/z value and try again
  Note: error of ~0.01-0.02 m/z is still a match, but the error should not be larger than this
  Hint: m/z gap should be ~57-186 to match an AA residue
Find the next biggest m/z peak and subtract it from the last peak you assigned, and then keep repeating this procedure until you get to lowest m/z peaks and can’t find more AA residues
  This will be the y ion series series
Start again from the precursor MH+ calculated in step 1 and subtract 18.02 (H2O). Then look for another gap that fits an AA residue mass and work your way down again looking for gaps that correspond to AA residues as in step 4
  This will be the b ion series
  Hint: in peptides produced by trypsin cleavage the first AA residue you find should be K or R
Reverse the order of the b series AA residues and align the 2 sequences!
For a deeper tutorial see http://ionsource.com/tutorial/DeNovo/introduction.htm
Notes: This is a very generalized workflow that is applied by groups working on proteomics using mass spectrometers
Broadly represents the most common method

## Slide 13: MS2 spectra -- Spectrum 1
488.78 x 2 = 977.56
- 1.008 = 976.55
M2H++  MH+
976.55
MH+
97.06
P
147.06
F
129.05
E
99.06
V
97.05
P
147.07
F
sequence from y ion series
PFEVPF..
sequence from b ion series
..EVPFLK
MH+ - 18.02 = 958.53
128.09
K
I/L
113.08
F
147.07
P
97.05
V
99.07
E
129.04
PFEVPFLK
(or PFEVPFIK)
A210622_bcc_hela_200ng_dda_1538.60512.60512.2_PFEVPFLK
Check results against theory here:
https://proteomicsresource.washington.edu/cgi-bin/fragment.cgi

## Slide 14: MS2 spectra -- Spectrum 2
449.29
510.28 x 2 = 1020.58
- 1.008 = 1019.57
M2H++  MH+
1019.57
MH+
128.09
K
163.06
Y
A210622_bcc_hela_200ng_dda_1538.21410.21410.2_VHVIFNYK
114.04
N
147.07
F
y ion series
VHVLFN..
b ion series
..VLFNYK
VHVIFNYK
113.09
I/L
99.06
V
MH+ - 18.02 = 1001.55
99.07
V
137.06
H
99.07
V
113.08
I/L
147.07
F
114.05
N

## Slide 15
Computer annotation – spectrum 1
A210622_bcc_hela_200ng_dda_1538.60512.60512.2_PFEVPFLK

## Slide 16
Computer annotation – spectrum 1
A210622_bcc_hela_200ng_dda_1538.60512.60512.2_PFEVPFLK

## Slide 17
Computer annotation – spectrum 2
A210622_bcc_hela_200ng_dda_1538.21410.21410.2_VHVIFNYK

## Slide 18
Computer annotation – spectrum 2
A210622_bcc_hela_200ng_dda_1538.21410.21410.2_VHVIFNYK